|  | Tower Crane Installation and Operation Verification Information Report |
| --- | --- |

| Project Name: |  | Project Owner: |  |
| --- | --- | --- | --- |
| Project Address: |  | Report Date: |  |
| Project GC/CM: |  | Type of Project: |  |
| Crane Mfr: |  | Crane Model #: |  |
| Anticipated Duration: |  | Reviewer: |  |

|  | Yes | No | N/A |
| --- | --- | --- | --- |
| 1 Professional engineered drawings and calculations been submitted and approved addressing and verifying the soil bearing capacity and ground stability surrounding the base of the tower crane to ensure it can safely sustain all the loading that maybe be applied during the course its operation? |  |  |  |
| Comments: |  |
| 1A Field inspections been conducted by qualified inspection engineering firm to confirm and document field conditions meet the requirements set forth in the approved engineered drawings? |  |  |  |
| Comments: |  |
| 2 Once erected is the crane along with its boom and jib free to weathervane 360 degrees without obstructions? |  |  |  |
| Comments: |  |
| 3 Are cranes equipped with fully functional wind speed sensors (anemometers)? If so, what is the maximum allowable in-service wind speed before the crane will be required to shut down? |  |  |  |
| Comments: |  |
| 4 Will a written wind action plan be developed and implemented? If so, provide a brief description of the wind action plan procedures. |  |  |  |
| Comments: |  |
| 5 If two or more tower cranes are operating at the same site are they erected to ensure there is no possibility that the boom and or jib sections will collide under any conditions of loading? |  |  |  |
| Comments: |  |
| 6 Professional engineering drawings and calculations been submitted and approved addressing the tower crane base foundation including but not limited to dimensions, concrete strength, size, and placement of reinforced steel to ensure the stability and strength of the structure will not be exceeded under the most severe static and dynamic crane loading condition? |  |  |  |
| Comments: |  |
| 6A Field inspections been conducted by qualified inspection engineering firm to confirm and document field conditions meet the requirements set forth in the approved engineered drawings? |  |  |  |
| Comments: |  |
| 7 Professional engineering drawings and/or manufacturer specifications and drawings been submitted and approved addressing base plate and anchor bolt size, locations and quality or any other anchoring system required to support the tower crane mast to the tower crane base foundation? |  |  |  |
| Comments: |  |
| 7A Field inspections been conducted by qualified inspection engineering firm to confirm and document field conditions meet the requirements set forth in the manufacturer’s specifications and/or approved engineered drawings? |  |  |  |
| Comments: |  |
| 8 Survey procedures in place to monitor on a regular basis any differential settlement of the tower cranes base foundation that could be caused by ground settlement. Have elevation readings been taken as soon as soon as possible after completion of crane erection and at regular intervals of 1 to 2 weeks thereafter. Has this information been documented? |  |  |  |
| Comments: |  |
| 9 Tower crane vertical mast and tower sections been erected as per manufacturer drawings and specifications and/or by approved engineered drawings and specifications completed by a professional engineer specializing in the field of crane engineering? |  |  |  |
| Comments: |  |
| 9A Field inspections been conducted by qualified inspection engineering firm to confirm and document field conditions meet the requirements set forth in the manufacturer’s specifications and/or approved engineered drawings? |  |  |  |
| Comments: |  |
| 10 Vertical tower mast sections been secured to the designated structure at the locations and heights as per manufacturer specifications and drawings and/or as per approved engineered drawings and specifications completed by a professional engineer specializing in the field of crane engineering that ensures the ties and frames are adequately designed and braced? |  |  |  |
| Comments: |  |
| 10A- Field inspections been conducted by qualified inspection engineering firm to confirm and document field conditions meet the requirements set forth in the manufacturer’s specifications and/or approved engineered drawings? |  |  |  |
| Comments: |  |
| 11 Engineering drawings and calculations been completed and submitted by a professional engineer specialized in the appropriate field that verifies the structure the tower crane is braced too is able to withstand additional forces that will be applied? |  |  |  |
| Comments: |  |
| 11A Field inspections been conducted by qualified inspection engineering firm to confirm and document field conditions meet the requirements set forth in the approved engineered drawings? |  |  |  |
| Comments: |  |
| 12 Determination and verification been made that the proper amount of counterweights have been installed for the specific crane, the jib length, and the type of operation the machine will be performing? |  |  |  |
| Comments: |  |
| 12A Field inspections been conducted by qualified inspection engineering firm to confirm and document field conditions meet the requirements set forth in the manufacturer’s specifications and/or approved engineered drawings? |  |  |  |
| Comments: |  |
| 13 Torque tests been conducted for all structural bolts as per manufacturer drawings and specifications and/or by approved engineered drawings and specifications completed by a professional engineer specializing in the field of crane engineering? |  |  |  |
| Comments: |  |
| 13A Field inspections been conducted by qualified inspection engineering firm to confirm and document field conditions meet the requirements set forth in the manufacturer’s specifications and/or approved engineered drawings? |  |  |  |
| Comments: |  |
| 14 Tower section jumping/climbing/dismantling procedures performed as per manufacturer approved drawings, protocols, and specification and or by approved engineered drawings and specifications completed by a professional engineer specializing in the field of crane engineering? |  |  |  |
| Comments: |  |
| 14A Field inspections been conducted by qualified inspection engineering firm to confirm and document field conditions meet the requirements set forth in the manufacturer’s specification and/or approved engineered drawings? |  |  |  |
| Comments: |  |
| 15 All tower crane components been clearly marked for proper identification during assembly and assurance made that only correct structural sections and components for that particular crane are used? |  |  |  |
| Comments: |  |
| 15A Field inspections been conducted by qualified inspection engineering firm to confirm and document field conditions meet the requirements set forth in the manufacturer’s specification and/or approved engineered drawings? |  |  |  |
| Comments: |  |
| 16 Have the main structural components of the crane been inspected and any damage or defects found repaired in accordance with the manufacturer’s specifications and instructions? |  |  |  |
| Comments: |  |
| 16A Field inspections been conducted by qualified inspection engineering firm to confirm and document field conditions meet the requirements set forth in the manufacturer’s specification and/or approved engineered drawings? |  |  |  |
| Comments: |  |
| 17 Have the electrical, mechanical, and hydraulic components been inspected to ensure they are in proper working order as per the manufacturer’s specification and instructions? |  |  |  |
| Comments: |  |
| 17A Field inspections been conducted by qualified inspection engineering firm to confirm and document field conditions meet the requirements set forth in the manufacturer’s specifications and/or approved engineered drawings? |  |  |  |
| Comments: |  |
| 18 Supervision of the tower crane erection, jumping and dismantling operations performed by an employee(s) of the responsible contractor who is qualified and trained in the field of tower cranes and has the knowledge and expertise to ensure the work is performed as per manufacturer specifications and/or approved engineering drawings? |  |  |  |
| Comments: |  |
| 19 Preconstruction meetings held with the construction tower crane erecting team prior to any tower crane erecting, jumping or dismantling operation to discuss and review procedures and protocols associated with these activities to ensure both operational and safety related issue/concerns have been addressed? |  |  |  |
| Comments: |  |
| 20 Are all employees of tower crane related activities who are engaged in rigging and/or hoisting related operations qualified and trained in proper rigging techniques? |  |  |  |
| Comments: |  |
| 21 At the completion of the initial tower crane erection operation is the services of an independent third-party crane engineering/inspection firm retained to perform a thorough inspection of the tower mast section and tower crane to ensure all work and components comply with requirements set forth in the manufacturer’s specifications and or approved engineering drawings? |  |  |  |
| Comments: |  |
| 22 During the jumping operation the services of an independent third-party crane engineering/inspection firm retained to perform a thorough inspection of this operation to ensure the work has been performed in accordance with manufacturer’s specifications and/or approved engineering drawings? |  |  |  |
| Comments: |  |
| 23 During the course of the project is the tower crane being inspected on a regular and frequent basis by a competent and qualified individual knowledgeable in the field of tower cranes to ensure the tower crane and tower mast sections continue to meet the requirements set forth in the manufacturer’s specifications and/or approved engineering drawings? |  |  |  |
| Comments: |  |
| 24 Are all inspections documented and retained at the construction site for review? |  |  |  |
| Comments: |  |
| 25 Are the cranes operators licensed, certified or hold any other valid credentials to operate the particular crane they are assigned to operate? |  |  |  |
| Comments: |  |
| 26 Are the weights of every hoisted load determined to ensure that based on the configuration of the crane including but not limited to radius, boom length, line pull and required deductions the hoisted load is within the safe working capacity of the crane based on the cranes load chart? |  |  |  |
| Comments: |  |
| 27 If tower crane is free standing have manufacturer drawings/specifications and/or engineered drawings completed by a professional engineer specialized in the field of crane engineering been submitted and approved identifying the maximum free-standing height? |  |  |  |
| Comments: |  |
| 27A Field inspections have been conducted by qualified inspection engineering firm to confirm and document field conditions meet the requirements set forth in the approved engineered drawings? |  |  |  |
| Comments: |  |